## Slide 1
ME8930 | AI for Composites and Manufacturing
AIM Composites
Materials Database
An AI-Assisted Repository for Composite Thermoplastic Property Data
Mathias Heider | Joint work with Abhijit (Clemson + UDel)
May 2026
Notes: Welcome everyone. Today I am presenting the AIM Composites Materials Database, an AI-assisted, open-source repository for thermoplastic composite property data built as part of ME8930. This is a joint effort between Clemson University and the University of Delaware. I will walk you through the motivation, the system we built, then we will do a live demo, and close with where this is headed.

## Slide 2
Today's Agenda
Mathias Heider | ME8930 Course Project | May 2026
Agenda
1
The Problem
Why ML for composites needs a better data foundation
2
Related Work
Existing databases & LLM extraction literature
3
What We Built
Architecture, schema, and deployment overview
4
Extraction Pipeline
PDF to structured rows via Gemini 2.5 Flash
5
User Workflows
Browse, manual upload, PDF-assisted upload
6
Current Data
289 rows, 4 materials, quality findings
7
LIVE DEMO
Walk through the running Hugging Face Space
8
Autonomous Ingestion
Batch prototype & path to fully automated ingestion
9
Next Steps
Provenance, evals, source discovery
Notes: Here is our road map for today. We will spend roughly 2 minutes each on the motivation, related work, and architecture sections, then go deeper on the extraction pipeline and user workflows. The live demo is in the middle. We will close with the autonomous ingestion work and next steps.

## Slide 3
The Data Bottleneck for ML in Composites
Mathias Heider | ME8930 Course Project | May 2026
1 / The Problem
PDF
Locked in PDFs
Manufacturer datasheets & journal papers are unstructured. No machine-readable format, no standardized column names.
DB
Sparse & Paywalled
Public databases (MatWeb, Granta MI) are costly, test-condition-poor, and sparse for thermoplastic composites.
GAP
No Open Standard
No widely accepted open repository for thermoplastic composite mechanical, thermal & processing data exists.
ML models for composites -- forward prediction, inverse design, process-quality -- all bottleneck on training data that does not exist in usable form.
Notes: The core motivation: machine learning for composites engineering -- forward property prediction, inverse design, process-quality modeling -- all share one bottleneck: training data. Property data is either locked inside PDFs, sparse and paywalled in commercial databases, or simply missing. This project is our attempt to close that gap.

## Slide 4
Related Work
Mathias Heider | ME8930 Course Project | May 2026
2 / Related Work
Existing Databases
MatWeb -- 160k+ materials; paywalled, no test conditions, sparse for thermoplastic composites.
Granta MI (Ansys) -- Most complete composites data, but enterprise-priced; focused on thermoset prepregs.
CMH-17 -- Authoritative aerospace allowables; not bulk-queryable; thermoplastics underrepresented.
NIST MDR -- Metals & ceramics focus; no open thermoplastic composite repository exists.
LLM Extraction Literature
ChemDataExtractor (2016+) -- NLP pipeline: 93% F-score on identifiers; used to extract 720k stress-strain records.
PropertyExtractor (Gupta 2024) -- Zero/few-shot with Gemini-Pro & GPT-4; dynamic extraction hierarchy refinement.
Liang et al. (2024) -- GPT-4 achieves F1 approx 0.91 on thermoelectric extraction; Gemini shows uneven quality on categoricals.
Structured-output prompting significantly reduces hallucination vs. free-text generation -- the design choice we adopted.
Gap: No open, FAIR-compliant, queryable database for thermoplastic composite experimental data.
Notes: To put our work in context: existing databases all have serious limitations for thermoplastic composites research. On the extraction side, the literature has moved from NLP rule systems toward LLM-based approaches. Structured output prompting -- which is what we use with Gemini -- substantially reduces hallucination. The gap we fill: there is no open, FAIR-compliant, queryable repository for this material class.

## Slide 5
What We Built -- System at a Glance
Mathias Heider | ME8930 Course Project | May 2026
3 / Architecture
STORAGE
DB
PostgreSQL
3 EAV tables
Polymers | Fibers
Composites
->
APPLICATION
APP
Streamlit
Home | Search
Upload | Contact
SQLAlchemy layer
->
AI PIPELINE
AI
Gemini 2.5 Flash
PDF to JSON
Schema-typed output
Temp = 0, structured
->
DEPLOYMENT
HF
Hugging Face Spaces
Docker container
python:3.11-slim
Public & open-source
Public on HF Spaces
|
289 property rows loaded
|
4 polymer materials
|
Open-source repo
Notes: The system has three main layers. PostgreSQL stores everything using an entity-attribute-value schema. A Streamlit web application sits on top with four pages. The AI pipeline is Gemini 2.5 Flash with structured JSON output. The whole thing runs as a public Docker container on Hugging Face Spaces. The URL is huggingface.co/spaces/aim4composites/MaterialsDatabase.

## Slide 6
Database Design -- EAV Schema
Mathias Heider | ME8930 Course Project | May 2026
3 / Architecture
Column
Description
material_name
Generic material name
material_abbreviation
Short ID (e.g., PEEK)
section
Property category (Mechanical, Thermal, ...)
property_name
Canonical or free-text property
value
Measured value or range (text)
unit
SI unit string
english
Imperial equivalent, when reported
test_condition
Temp, strain rate, standard, geometry
comments
Notes, footnotes, standard references
Why EAV?
> Sparse data
Any given datasheet covers only a subset of properties. Wide tables would be mostly NULLs.
> Open taxonomy
New properties appear routinely. EAV adds rows; wide tables require schema migrations.
> Per-row provenance
Each observation has its own test conditions and source -- keeping them in-row avoids a messy join.
> Three material classes
Polymers, Fibers, Composites each map to a table; class encoded by table membership.
Notes: The database uses an entity-attribute-value layout: each property observation is one row. We have three tables sharing this schema. Why EAV? First, composite property data is inherently sparse. Second, the property taxonomy is open. Third, each measurement has its own test conditions. The tradeoff is that aggregation queries require filtering on property_name rather than selecting a column, and unit consistency must be enforced application-side.

## Slide 7
PDF to Structured Rows via Gemini 2.5 Flash
Mathias Heider | ME8930 Course Project | May 2026
4 / Extraction Pipeline
1
PDF In
User drops datasheet or paper.
Base64-encoded and sent inline.
->
2
Schema-typed Prompt
responseSchema enforces fixed JSON shape.
Temp = 0 for determinism.
->
3
Expert Prompt
Frames model as materials scientist; enumerates all per-property fields across Mechanical, Thermal, Electrical, Physical, Optical, Rheological.
->
4
Flatten to DataFrame
Response flattened to DataFrame matching EAV schema. Plot images extracted in parallel via PyMuPDF + OpenCV.
Key implementation details
responseMimeType: application/json -- forces valid JSON. temperature: 0 -- deterministic extraction. Required fields -- model emits empty string for missing values, never null. english field -- passthrough for imperial values when source reports both.
Notes: The heart of the system is the Gemini extraction pipeline. A user drops a PDF. We base64-encode it and send it inline to Gemini 2.5 Flash. The key design choice is structured output: we supply a responseSchema that forces a fixed JSON shape, and we set temperature to 0 for determinism. The system prompt frames the model as an expert materials scientist and asks for every property type in a single flat list. The JSON response is flattened into a pandas DataFrame that maps directly onto the EAV schema. In parallel, PyMuPDF and OpenCV run a plot-extraction pass that finds figures and maps them to property rows.

## Slide 8
User-Facing Workflows
Mathias Heider | ME8930 Course Project | May 2026
5 / User Workflows
Browse / Search
1
Select material class (Composite / Polymer / Fiber)
2
Filter by matrix or fiber (composites)
3
Search by name or abbreviation
4
Paginated results grid (50 per page)
5
Inspect tab: property table + plot image
Manual Upload
1
Pick material class then property category
2
Select canonical property name (or free text)
3
Enter value, unit, English equiv., test condition
4
Comments field for notes & standards
5
Single row written to Postgres
PDF-Assisted Upload
1
Drag PDF (datasheet or paper)
2
Gemini extracts all properties: preview table
3
User assigns material class
4
Review rows then click Add to Database
5
Plot figures mapped to properties in second tab
Notes: There are three ways users interact with the database. First, browsing: the Categorized Search page. Second, manual upload: a form-based entry mode. Third, PDF-assisted upload: the main ingestion path. Drag in a PDF, Gemini extracts all properties, you review the table, assign a class, and insert. This is still human-in-the-loop but we are working to automate it.

## Slide 9
Current Data & Data-Quality Findings
Mathias Heider | ME8930 Course Project | May 2026
6 / Current Data
Loaded in Seed
4
Polymer materials
289
Property rows
6
Sections observed
PTFE | ABS | PEKK | Nylon 66
Fibers + Composites tables: empty
Data-Quality Issues Found
!
Unit inconsistency
Some rows omit unit key; others store units inline in the value string -- breaks numeric parsing.
!
Mixed unit systems
SI/English mixed within a single value field; intended: SI in value, imperial in english column.
!
Duplicate property rows
Same property at different test conditions -- correct behavior, but blocks naive UNIQUE constraint.
!
No source attribution
No PDF / DOI / page-number column today. Provenance captured informally in comments at best.
Notes: The current seed data covers four engineering thermoplastics: PTFE, ABS, PEKK, and Nylon 66, giving us 289 property rows across six sections. The Fibers and Composites tables are empty. During seed review we found four recurring quality issues: unit inconsistency, mixed unit systems, duplicate rows at different test conditions -- correct behavior but complicates schema constraints -- and most critically, no source attribution. Adding provenance is the highest-priority schema change.

## Slide 10
Material Taxonomy & Property Sections
Mathias Heider | ME8930 Course Project | May 2026
3 / Architecture
Polymers
PEEK | PEI | PA66 | ABS | PTFE | PEKK
Fibers
Carbon | Glass | Aramid | Basalt | Natural fibers
Composites
Fiber-reinforced laminates & molding compounds
(Matrix + fiber + Vf + architecture + process)
Property Sections (per material class)
Mechanical
Thermal
Electrical
Physical
Optical
Rheological
Processing
Descriptive
Composition / Reinforcement
Architecture / Structure
* Composites only
Notes: The material taxonomy organizes everything into three classes. Within each class, properties are grouped into up to ten sections. Within each section, users choose from a curated list of canonical property names plus a free-text fallback. This normalization keeps property names consistent for downstream ML queries.

## Slide 11
>> LIVE DEMO
AIM Composites
Materials Database
huggingface.co/spaces/aim4composites/MaterialsDatabase
1 Browse polymers -> inspect PEEK properties
2 Upload a PDF datasheet -> review Gemini extraction
3 Map a figure to a property row
4 Run batch_ingest.py on a test corpus
Mathias Heider | ME8930 Course Project | May 2026
7 / LIVE DEMO (~7 min)
Notes: PAUSE HERE FOR LIVE DEMO -- approximately 7 minutes. Demo script: 1. Open huggingface.co/spaces/aim4composites/MaterialsDatabase in browser. 2. Browse -> show PEEK material -> Inspect tab -> scroll through property rows, show a plot image. 3. Upload -> PDF-assisted -> drag in a test datasheet -> show Gemini extraction -> walk through the review table. 4. Map a detected figure to a property row. 5. Terminal -- show batch_ingest.py run on a small PDF folder. Key talking points: everything is live, open-source, and publicly deployed.

## Slide 12
Closing the Loop -- Toward Autonomous Ingestion
Mathias Heider | ME8930 Course Project | May 2026
8 / Autonomous Ingestion
1
DISCOVER
Semantic Scholar
OpenAlex | arXiv
Relevance ranking + download
Planned
->
2
EXTRACT
Gemini 2.5 Flash
Schema-typed JSON
Production-ready today
Ready
->
3
VALIDATE
Unit normalization
Plausibility ranges
Dedup by (material, prop, cond)
Ready
->
4
INSERT
Postgres write
Provenance FK
Failed rows -> review queue
Ready
Prototype today: batch_ingest.py covers steps 2-4 on a fixed PDF corpus, without source discovery. Commits to a SQLite mirror so the prototype runs offline without touching production Postgres.
Notes: The vision is to close the ingestion loop completely. The target is a four-component autonomous agent: source discovery, extraction (already production-ready), validation, and insertion with provenance tracking. Our batch_ingest.py prototype already covers steps 2 through 4. Step 1 -- source discovery -- is the next piece to build.

## Slide 13
Batch Ingestion Prototype -- Results
Mathias Heider | ME8930 Course Project | May 2026
8 / Autonomous Ingestion
10-25s
per PDF
(Gemini latency)
~15%
rows flagged:
missing unit
(mostly false positives)
5-10%
rows flagged:
inline-unit value
(real format issue)
0
new rows on
re-ingest of
same PDF
(dedup works)
Chart: 
| Passed | Missing unit (dim-less) | Inline unit value | Out-of-range
% of rows | 76 | 15 | 8 | 1
Notes: Here are the preliminary numbers. Gemini processing takes 10 to 25 seconds per PDF. Validation flags split into three buckets: about 15% flagged for missing units -- but most are dimensionless quantities, so false positives. Around 5-10% flagged for inline-unit values -- a real format inconsistency. A small number have out-of-range numerics. Crucially, deduplication works: re-ingesting a previously seen PDF inserts zero new rows. These numbers are indicative, not rigorous -- a hand-labeled ground truth set is needed.

## Slide 14
Known Limitations
Mathias Heider | ME8930 Course Project | May 2026
8 / Autonomous Ingestion
01
No Provenance
No source PDF, DOI, or page-number column. Adding a sources table with FK references is the highest-priority schema change.
02
Schema Rigidity
Cure schedules, processing windows, and stress-strain curves do not fit one-row-per-property. Stored as free text or PNG plot images.
03
Keyword Class Routing
Material class assigned by keyword matching on material_name. Prone to errors on ambiguous names -- needs a small classifier.
04
No Evaluation Set
Extraction precision/recall not formally measured. A 50-100 row hand-labeled ground-truth set is needed before publishing accuracy numbers.
05
No Source Discovery
Batch prototype works on a fixed PDF folder. Source discovery (OpenAlex, Semantic Scholar, arXiv) is not yet implemented.
06
Empty Tables
Fibers and Composites_materials tables contain zero rows in the current seed. The database is polymer-only today.
Notes: Being honest about limitations: there are six areas where the system falls short today. Most critically, there is no provenance -- we do not record where a property value came from. Schema rigidity means multi-dimensional data does not fit the EAV model cleanly. Class routing by keywords is fragile. We have not measured extraction precision and recall. Source discovery is not built yet. And the database is polymer-only.

## Slide 15
Next Steps & Future Work
Mathias Heider | ME8930 Course Project | May 2026
9 / Next Steps
P0
Add sources table + provenance
Every inserted row gets a FK to a sources table tracking PDF hash, DOI, and page number. Critical for reproducibility.
P1
Hand-label evaluation set
50-100 row gold-standard ground truth for extraction precision/recall. Required before publishing accuracy numbers.
P1
Classifier for class routing
Replace keyword heuristic with a small classifier on extracted material name + properties. Fewer misrouting errors.
P2
Source discovery agent
OpenAlex / Semantic Scholar / arXiv APIs with paper-relevance scoring. Closes the final loop in autonomous ingestion.
P2
Config-driven validation rules
Move plausibility ranges to a YAML/JSON config so domain experts can edit them without touching code.
P3
Populate Fibers + Composites
Systematic ingestion of fiber and laminate datasheet corpora. Unlocks the full three-class taxonomy for ML training.
Notes: The next steps are organized by priority. P0 -- most urgent -- is adding provenance tracking. P1 covers the evaluation set and the classifier. P2 adds source discovery and config-driven validation rules. P3 is systematic ingestion of fibers and composites datasheets to unlock the full taxonomy for ML training. The project is actively developed and the codebase is fully open on Hugging Face.

## Slide 16
Thank you!
Questions?
Mathias Heider
mathias.heider@gmail.com
App: huggingface.co/spaces/aim4composites/MaterialsDatabase
Joint work with Abhijit -- Clemson University + University of Delaware
Acknowledgments: Joint research with Abhijit (AbhijitClemson) and the AIM Composites team. Thanks to the ME8930 instructor for framing the autonomous-AI question and to Google for Gemini API credits.
Notes: Thank you. I would love to take questions on the schema design, the Gemini extraction approach, the autonomous agent architecture, or anything else. The app is live at the URL on screen if you want to try it yourself. The codebase is fully open-source.